## Slide 1: EE305 Power Electronics
Dr. Unnikrishnan P.C.
Professor, EEE

## Slide 2
Choppers

## Slide 3: What is a Chopper?
Converter that converts a constant DC voltage to a variable DC voltage
Also known as DC-DC converter
Done by switching the source ON and OFF periodically
Widely used in trolley cars, battery operated vehicles, traction motor control, control of large number of dc motors, etc…

## Slide 4: Step down chopper
Principle of Operation
tON- ON time of switch and
tOFF- OFF time of switch
The average output voltage:

## Slide 5: Step down chopper
Average value of the load current for resistive load

## Slide 6: Control of Output Voltage Time Ratio control(TRC)
For the control of output voltage two methods
  Constant frequency TRC
  Variable frequency TRC
    Constant tON
    Constant tOFF

## Slide 7: Constant frequency TRC Also Called “pulse width modulation scheme”
Chopping frequency kept constant and tON varied

## Slide 8: Variable frequency TRC(Constant ton) Also called “frequency modulation scheme”
Keeping tON constant and varying tOFF i.e. Varying f

## Slide 9: Variable frequency TRC(Constant toff) Also called “frequency modulation scheme”
Keeping tOFF constant and varying tON i.e. Varying f

## Slide 10: Variable frequency TRC
Disadvantages:
Generates harmonics of different frequencies and hence requires large filters
To control the duty cycle,, frequency variation would be wide. This might create interference with signalling and telephone lines.
The large OFF-time in this scheme may make the load current discontinuous which is undesirable.
A fixed frequency Chopper is generally used

## Slide 11: Current limit control
Load current maintained between an upper level and lower level.
When the load current reached the upper limit, the chopper switch is turned OFF, the load current decays to the lover limit through a free wheeling diode. The load current is continuous- possible only with high inductive loads

## Slide 12: Step-Down Chopper

## Slide 13: Step-Down Chopper
Chopper Switch kept ON for tON and the energy is stored in the inductor
As the switch is turned OFF, the free wheeling diode is forward biased and the load current continues to flow due to the energy stored in the inductor.
The chopper switch is turned ON when load current reaches a lower limit
Load voltage and load current are positive and the power flows from the source to the load. So it is also called a first quadrant chopper or class A chopper

## Slide 14: Step-Down Chopper